# CHAPTER IV

25

# SOFTWARE DEVELOPMENT

# 4.1 ALGORITHM

1. Start the program.

2. Assume Port1 as input port and Port3 as output port.

3. Initially set the pins of Port1 and Port3 to contain ‘0’.

4. Check if any bit is available in the Port1.

5. If the bits are available in the Port1, check the bits for right or left, up or down, Clipper open or clipper close motion of arm.

6. Activate the control signal according to the required motion and   GOTO Step 8.

7. If no bit is available at the Port 1 repeat the process from Step 4.

8. Stop the execution.

26

4.2 FLOWCHART

NO

NO

NO

NO

NO

NO

4.3 PROGRAM

o1  equ p3.0

o2  equ p3.1

o3  equ p3.2

o4  equ p3.3	    ASSIGNING PORT 3 PINS

o5  equ p3.4

o6  equ p3.5

org  0000h

mov sp,#040h

clr o1

clr o2

clr o3                           INITIALIZING ‘0’ FOR PORT1 AND PORT3 PINS

clr o4

clr o5

clr o6

mov p3,#000h

start:

oo1:

mov a,p1		   MOVE PORT1 TO ACCUMULATOR

cjne  a,#01h,oo2	   COMP AND JMP IF NOT EQUAL TO ZERO oo2

setb o1		   SET o1 TO B REGISTER

acall sdelay	   CALLING SDELAY LOOP

clr  o1		   CLEAR o1

acall ldelay	   CALLING LDELAY LOOP

acall ldelay	   CALLING LDELAY LOOP

oo2:

mov a,p1		  MOVE PORT1 TO ACCUMULATOR

cjne  a,#02h,oo3    COMP AND JMP IF NOT EQUAL TO ZERO oo3

setb o2	SET o2 TO B REGISTER

acall sdelay	CALLING SDELAY LOOP

clr  o2	CLEAR o2

acall ldelay	CALLING LDELAY LOOP

acall ldelay	CALLING LDELAY LOOP

oo3:

mov a,p1		  MOVE PORT1 TO ACCUMULATOR

cjne  a,#04h,oo4     COMP AND JMP IF NOT EQUAL TO ZERO oo4

setb o3                    SET o3 TO B REGISTER

acall sdelay             CALLING SDELAY LOOP

clr  o3                      CLEAR o3

acall ldelay              CALLING LDELAY LOOP

acall ldelay              CALLING LDELAY LOOP

28

oo4:

mov a,p1		   MOVE PORT1 TO ACCUMULATOR

cjne  a,#08h,oo5     COMP AND JMP IF NOT EQUAL TO ZERO oo5

setb o4                      SET o4 TO B REGISTER

acall sdelay              CALLING SDELAY LOOP

clr  o4                      CLEAR o4

acall ldelay              CALLING LDELAY LOOP

acall ldelay              CALLING LDELAY LOOP

oo5:

mov a,p1		    MOVE PORT1 TO ACCUMULATOR

cjne  a,#03h,oo6      COMP AND JMP IF NOT EQUAL TO ZERO oo6

setb o5	 SET o5 TO B REGISTER

acall sdelay	CALLING SDELAY LOOP

clr  o5	CLEAR o5

acall ldelay              CALLING LDELAY LOOP

acall ldelay              CALLING LDELAY LOOP

oo6:

mov a,p1		   MOVE PORT1 TO ACCUMULATOR

cjne  a,#07h,ood      COMP AND JMP IF NOT EQUAL TO ZERO ooD

setb o6	SET o6 TO B REGISTER

acall sdelay	CALLING SDELAY LOOP

clr  o6	CLEAR o6

acall ldelay               CALLING LDELAY LOOP

acall ldelay               CALLING LDELAY LOOP

ood:

ajmp start

sdelay:         mov     r5,#020h  	 MOV #020H TO REGISTER R5

sdelay0:        djnz    r6,sdelay0 	DEC REG-6  AND JMP IF NOT ZERO

djnz    r5,sdelay0                  DEC REG-6  AND JMP IF NOT ZERO

ret                                          RETURN

ldelay:         mov     r5,#060h   	MOV #060H TO REGISTER R5

ldelay0:        djnz    r6,ldelay0 	DEC REG-6  AND JMP IF NOT ZERO

djnz    r5,ldelay0                  DEC REG-6  AND JMP IF NOT ZERO

ret		                        RETURN

end

29

# Text boxes

START

INTIALISE

PORT1 AS INPUT

PORT3 AS OUTPUT

SET

PORT 1 = 0

PORT 3 = 0

MOV A, P1

IF

A = #01h

LEFT

RIGHT

IF

A = #02h

UP

IF

A = #03h

DOWN

IF

A = #04h

CLIPPER OPEN

IF

A = #05h

CLIPPER CLOSE

IF

A = #06h

STOP

YES

YES

YES

YES

YES

YES